## Slide 1
Smart Motion Drive
for the Future Mobility
Team Name: Blooming

## Slide 2: Background
Web 4.0 will integrate the digital world and the real world.
Autonomous driving is one of the key technologies.
An inclusive society is needed where seniors and people with disabilities can live safely and joyfully.
Elderly People
People with Disabilities
New Technology for INCLUSIVE MOBILITY!
To achieve this, we propose:

## Slide 3: How to Realize Inclusive Mobility
Capture your motion using motion capture device (mocopi†).
Six sensors are attached to key points of your body.
User motions are recognized as commands for an autonomous car.
  Raise Right Hand Call
  Raise Left Hand Return
Sensor
†https://www.sony.jp/mocopi/
You can control a car with your body motion!

## Slide 4: Overview of Our System
Capture Your Motion
Send Motion
Send Command
Control a Car
(e.g., Acceleration)
Move a Car with Your Motion
(e.g., Call)
mocopi
Smart Motion Drive
Application (Unity)
Smart Motion Plugin
(Python)
UC-win/Road
Our Developed System
You

## Slide 5: Smart Motion Drive Application (Unity)
The avatar synchronizes with your motion.
You can select two drive modes.
  Self-driving mode
  Auto-driving mode

## Slide 6: Self-Driving Mode
Command | User Motion | Description
Accel | Raise Right Hand | Move the car forward.
Back | Raise Left Hand | Move the car backward.
Stop | Push Right Hand Forward | Stop the car.
Turn Right | Move Right Hand to the Right Side | Turn the car to the right.
Turn Left | Move Left Hand to the Left Side | Turn the car to the left.
Motions for Self-Driving Mode
Control Patterns for Self-Driving Mode
Your motions are recognized as the following five commands.

## Slide 7: Auto-Driving Mode
Control Pattern | User Motion | Description
Call | Raise Right Hand | Call a car to your location.
Return | Raise Left Hand | Send the car back to a parking area.
Stop | Push Right Hand Forward | Stop the car.
Motions for Auto-Driving Mode
Control Patterns for Auto-Driving Mode
Your motions are recognized as the following three commands.

## Slide 8: Application Scenario
Your Car
You
Your car is in a parking area.
You want to call it to your side while standing outside the car.

## Slide 9: Demo: Self-Driving Mode

## Slide 10: Demo: Auto-Driving Mode

## Slide 11: Conclusions
Smart Motion Drive creates a new way of interaction between people and autonomous cars.
It empowers seniors and people with disabilities with joyful mobility.
Our goal is to design
inclusive mobility for the Web 4.0 era.
Have fun with our Smart Motion Drive!